Product Overview

The CORONET® Donor Trephine Punch has been specifically designed to deliver a reliable and consistent vertical incision, giving improved wound architecture and reduced endothelial cell loss.

The free rotating trephine features exclusive CORONET® Cathedral Blade Technology, creating an ultra-thin and sharp blade which minimises undercut and tissue distortion

- Complete donor graft preparation system suitable for PK, DALK and DSAEK/DSEK surgery

- Sharp, clean cutting action requires minimal downward pressure to complete the cut

- Ultra-sharp and thin blade produces a vertical cut that improves approximation between the donor button and patient cornea

- Patent protected 360˚ graft visualisation windows, for increased accuracy

- Double sided Cathedral blade will not retain graft button once cut

- Anatomically shaped bowl to gently support the tissue and aid centralisation

- Marker holes to reduce risk of bubble formation

- Unique base provides a stable platform which can be easily held in place during donor preparation

- Non-glare all metal construction blade

- Supplied with protective dust cover, to shield graft from contamination during transfer from donor to patient

- Supplied sterile, single use only, one per box, declared 5-year shelf life

- Available with or without vacuum

- Manufactured in the UK

Donor Trephine Size Options

| Trephine Size (mm) | 51-835 | 51-850 |
| --- | --- | --- |
| 6.00 | 51-835-6.00 | 51-850-6.00 |
| 6.25 | 51-835-6.25 | 51-850-6.25 |
| 6.50 | 51-835-6.50 | 51-850-6.50 |
| 6.75 | 51-835-6.75 | 51-850-6.75 |
| 7.00 | 51-835-7.00 | 51-850-7.00 |
| 7.25 | 51-835-7.25 | 51-850-7.25 |
| 7.50 | 51-835-7.50 | 51-850-7.50 |
| 7.75 | 51-835-7.75 | 51-850-7.75 |
| 8.00 | 51-835-8.00 | 51-850-8.00 |
| 8.25 | 51-835-8.25 | 51-850-8.25 |
| 8.50 | 51-835-8.50 | 51-850-8.50 |
| 8.75 | 51-835-8.75 | 51-850-8.75 |
| 9.00 | 51-835-9.00 | 51-850-9.00 |
| 9.25 | 51-835-9.25 | 51-850-9.25 |
| 9.50 | 51-835-9.50 | 51-850-9.50 |
| 9.75 | 51-835-9.75 | 51-850-9.75 |

Material Specification

| Product Component | Specification |
| --- | --- |
| Trephine Blade | Stainless Steel |
| Trephine Body | Aluminium |
| Punch Base | Polycarbonate |
| Syringe with luer | Polycarbonate, Luer-Lok (5ml capacity) |
| Blister Packaging | 0.5mm PETG Blister/ TYVEK Lid (122mm x 188mm) |
| Outer Box/Carton | 500 Micron Printed White Boxboard |

## Intended Use

The CORONET® Donor Trephine punch is designed specifically for preparing donor graft tissue. Each Trephine is designated for ‘SINGLE USE ONLY’ and should not be re-sterilised by any method or re-used.

Instructions for Use

The instructions for use and suggested surgical technique are supplied in the form of a multi-lingual leaflet with instructions given in diagram form where appropriate. The international symbols used on the packaging are explained in each language. A leaflet is supplied with each product

## Sterilisation

Products are sterilised by Ethylene Oxide (EO) according to a validated cycle and the requirements of BS EN ISO 11135-1 (current).

Conformity to the European Directives

All CORONET® Corneal Trephines are classified as a surgically invasive device intended for transient use, (Rule 6, Annex IX 93/42/EEC Medical Devices Directive, as amended by 2007/47/EEC) and is therefore classified as a Class IIa device.